## Slide 1: Proposal to Align oneCCL APIs with NCCL and HCCL Gengbin Zheng, Maria Garzaran, Blazej Smorawski

## Slide 2: OneCCL Library
Provides an efficient implementation of collective communication patterns
The library is integrated into DL framework stacks (PyTorch, TensorFlow)
Built on top of lower-level communication middleware
  MPI and libfabric to transparently support many interconnects, such as InfiniBand, Cassini, Intel Ethernet, an others.
  Level Zero and SYCL kernels for GPU communication/kernel spawning
  Optimized for high performance on Intel® CPUs and GPUs.

## Slide 3: New OneCCL API Design Goals
NCCL-like API for easy adoption
Improved ABI compatibility with the C APIs
Support single package for all supported hardware
  Use plugins approach, which can be assigned to each communicator

## Slide 4: New OneCCL API Overview
Major changes to the current oneCCL C++ interface
  Most APIs are C APIs that are similar to NCCL
    C++ structures are hidden behind the handles returned to the user
      e.g. ccl::stream and ccl::comm
  Extension C++ API functions to support sycl::queue
    onecclResult_t onecclCreateStream(sycl::queue, &oneccl_stream)
    onecclResult_t onecclReleaseStream(oneccl_stream)
    Sycl::queue once registered, will be hidden behind the ccl stream handle
  Add functions to allow users to explicitly control the lifetime of objects, instead of relying on the C++ destructors
    onecclResult_t onecclCommFinalize(comm)
    onecclResult_t onecclCommDestroy(comm)
  Drop support for out-of-order SYCL queue and SYCL buffers

## Slide 5
NCCL Comm Calls | oneCCL (proposed) | oneCCL (current C++) | HCCL
cudaError_t cudaSetDevice(device) | onecclResult_t onecclSetDevice(device) | N/A | 
ncclResult_t ncclGetUniqueId (id) | onecclResult_t onecclGetUniqueId (id) | ccl::create_main_kvs(); ccl::create_kvs(main_addr); | hcclResult_t hcclGetUniqueId (id)
ncclResult_t ncclCommInitRank (comm, size, id, rank) | onecclResult_t onecclCommInitRank (comm, size, id, rank) | comm ccl::create_communicator (size, rank, device, context, kvs) comms ccl:create_communicators (size, rank, device, context, kvs) | hcclResult_t hcclCommInitRank (comm, size, id, rank)
ncclResult_t ncclCommInitRankConfig (comm, size, id, rank, attr) | onecclResult_t onecclCommInitRankConfig (comm, size, id, rank, attr) | comm ccl:create_communicator (size, rank, device, context, kvs, attr) | N/A
ncclResult_t ncclCommInitAll (comms, ndev, dev_list) | onecclResult_t onecclCommInitAll (comms,ndev,dev_list) |  | N/A
ncclCommSplit | Not implemented |  | N/A
nccltResult ncclCommFinalize (comm) | onecclResult_t onecclCommFinalize (comm) | N/A | hcclResult_t hcclCommFinalize (comm)
ncclResult_t ncclCommDestroy (comm) | onecclResult_t onecclCommDestroy (comm) | Destructor | hcclResult_t hcclCommDestroy (comm)
Experimental
(WIP)
Notes: Platform context (check Greg’s email)
Keep the device parameter in the comm calls, to avoid an extra call in oneCCL
Do we do the APIs? Yes, so that we are aligned
When? By the end of the year.
kvs:get_address  could be simplified to be similar
ncclCommInitrank does not contain the device, but CUDA has a function CudaSetDevice(process) and CudaGetDevice(process)
  In addition, Intel GPUs require a context.
We could have the stream on the communicator instead of the device/context (with the stream, we can retrieve the device and context)
  https://github.com/intel-innersource/libraries.performance.communication.oneccl/blob/8da45be5953fcf7c47bcf47cfc6d79b452c5d456/src/comm/comm.hpp#L294C5-L294C27
nccltResult. ncclCommFinalize (comm). How useful is this? I assume you can wait on a queue? But do you need to wait on the communicator? Is this to destroy the communicator.
ncclResult_tncclCommFinalize(ncclComm_t comm).-> Check status on a non-blocking communicator. It is called really to complete the operations on the communicator
ncclGetAsyncError  It is used to query progress and potential errors.
NCCL has return values for NCCL functions. oneCCL error handling is different because it is based on C++ exception
Common exceptions
Exception class
Description
ccl::exception: Reports general unspecified error
ccl::invalid_argument. Reports an error when arguments to the operation were rejected
ccl::host_bad_alloc. Reports an error that occurred during memory allocation on the host
ccl::unimplemented. Reports an error when the requested operation is not implemented
ccl::unsupported. Reports an error when the requested operation is not supported

## Slide 6
NCCL Comm Calls | oneCCL (proposed) | oneCCL (current C++) | HCCL
ncclResult_t ncclCommCount (comm, size) | onecclResult_t onecclCommCount (comm, size) | size communicator::size() | ncclResutl_t hcclCommCount (comm, size)
ncclResult_t ncclCommCuDevice (comm, device) | onecclResult_t onecclCommGetDevice (comm, device) | device communicator::get_device() | hcclResult_t hcclCommSynDevice (comm, device)
ncclResults_t ncclCommUserRank (comm, rank) | onecclResult_t onecclCommUserRank (comm, rank) | rank communicator::rank() | hcclResult_t hcclCommUserRank (comm, rank)
ncclResult_t ncclGetVersion (version) | onecclResult_t onecclGetVersion (version) | version ccl:get_library_version () | hcclResult_t hcclGetVersion (version)
ncclCommAbort | Not implemented |  | N/A
ncclCommGetAsyncError | Not implemented |  | hcclCommGetAsyncError
ncclGetLastError | Not implemented |  | N/A
ncclGetErrorString | Not implemented |  | N/A
Notes: kvs:get_address  could be simplified to be similar
ncclCommInitrank does not contain the device, but CUDA has a function CudaSetDevice(process) and CudaGetDevice(process)
  In addition, Intel GPUs require a context.
ncclResult_tncclCommFinalize(ncclComm_t comm).-> Check status on a non-blocking communicator. It is called really to complete the operations on the communicator
ncclGetAsyncError  It is used to query progress and potential errors.
NCCL has return values for NCCL functions. oneCCL error handling is different because it is based on C++ exception
ccl:commCount(communicator, &size)
Common exceptions
Exception class
Description
ccl::exception: Reports general unspecified error
ccl::invalid_argument. Reports an error when arguments to the operation were rejected
ccl::host_bad_alloc. Reports an error that occurred during memory allocation on the host
ccl::unimplemented. Reports an error when the requested operation is not implemented
ccl::unsupported. Reports an error when the requested operation is not supported

## Slide 7: Collective Communication Calls
NCCL | oneCCL (proposed) | oneCCL (current C++) | HCCL
ncclResult_t ncclAllgather (sendbuff, recvbuff, count, datatype, op, comm, stream) | onecclResult_t onecclAllgather (sendbuff, recvbuff, count, datatype, op, comm, oneccl_stream) | ccl::event communicator::allgather(sendbuff, recvbuff, count, datatype, op, comm, oneccl_stream, deps) | hcclAllGather
ncclAllreduce | onecclAllreduce | communicator::allreduce | hcclAllreduce
ncclBroadcast | onecclBroadcast | communicator::broadcast | hcclBroadcat
ncclReduce | onecclReduce | communicator::reduce | hcclReduce
ncclReduceScatter | onecclReduceScatter | communicator::reduce_scatter | hcclReduceScatter
N/A | onecclAlltoall onecclAlltoallv We could deprecate | communicator::alltoall communicator::alltoallv | hcclAlltoAll
N/A | onecclBarrier We could deprecate and use Allreduce with 1 Byte | communicator::barrier | N/A
Notes: typedef __device_builtin__ struct CUStream_st *cudaStream_t;
https://stackoverflow.com/questions/49102916/how-big-is-a-cudastream-t
oneCCL currently also has allgatherv, which we can deprecate, but maintain for PVC for better performance

## Slide 8
Group APIs | oneCCL (proposed) | oneCCL (current) | HCCL
ncclResult_t ncclGroupStart() | onecclResult_t onecclGroupStart() | N/A | hcclResult_t hcclGroupStart()
ncclResult_t ncclGroupEnd() | onecclResult_t onecclGroupEnd() | N/A | hcclResult_t hcclGroupEnd()
Point to Point APIs | oneCCL (proposed) | oneCCL (current) | HCCL
ncclResult_t ncclSend(sendbuf, count, datatype, peer, comm, stream) | onecclResult_t onecclSend(sendbuf, count, datatype, peer, comm, oneccl_stream) | ccl::event communicator::send(sendbuf, count, datatype, peer, comm, oneccl_stream) | hcclResult_t hcclSend(sendbuf,count,datatype, peer, comm, stream)
ncclResult_t ncclRecv(…) | onecclResult_t onecclRecv(…) | communicator::recv | hcclResult_t hcclRecv(….)
Notes: kvs:get_address  could be simplified to be similar
ncclCommInitrank does not contain the device, but CUDA has a function CudaSetDevice(process) and CudaGetDevice(process)
  In addition, Intel GPUs require a context.
ncclResult_tncclCommFinalize(ncclComm_t comm).-> Check status on a non-blocking communicator. It is called really to complete the operations on the communicator
ncclGetAsyncError  It is used to query progress and potential errors.
NCCL has return values for NCCL functions. oneCCL error handling is different because it is based on C++ exception // Błażej: We might have to create some small wrapper to call oneCCL API and catch all exceptions. Should not be too hard
Common exceptions
Exception class
Description
ccl::exception: Reports general unspecified error
ccl::invalid_argument. Reports an error when arguments to the operation were rejected
ccl::host_bad_alloc. Reports an error that occurred during memory allocation on the host
ccl::unimplemented. Reports an error when the requested operation is not implemented
ccl::unsupported. Reports an error when the requested operation is not supported

## Slide 9
NCCL Comm Calls | oneCCL | HCCL
ncclCommRegister | Not implemented | N/A
ncclCommDeregister | Not implemented | N/A
ncclMemAlloc | Not implemented | N/A
ncclMemFree | Not implemented | N/A
These (and all the not implemented ones) can be added as needed
Notes: kvs:get_address  could be simplified to be similar
ncclCommInitrank does not contain the device, but CUDA has a function CudaSetDevice(process) and CudaGetDevice(process)
  In addition, Intel GPUs require a context.
ncclResult_tncclCommFinalize(ncclComm_t comm).-> Check status on a non-blocking communicator. It is called really to complete the operations on the communicator
ncclGetAsyncError  It is used to query progress and potential errors.
NCCL has return values for NCCL functions. oneCCL error handling is different because it is based on C++ exception // Błażej: We might have to create some small wrapper to call oneCCL API and catch all exceptions. Should not be too hard
Common exceptions
Exception class
Description
ccl::exception: Reports general unspecified error
ccl::invalid_argument. Reports an error when arguments to the operation were rejected
ccl::host_bad_alloc. Reports an error that occurred during memory allocation on the host
ccl::unimplemented. Reports an error when the requested operation is not implemented
ccl::unsupported. Reports an error when the requested operation is not supported

## Slide 10: Support for CPU
Working on extensions to make it very close to the GPU, without additional parameters
Working on some APIs mostly for CPU, but could be used in the GPU desired
  Mostly to wait or test if the operations are completed